Bode Plots by hand and by MatLab

1. Bode Plots by Hand

Bode Phase Plots

Page 3

2. Bode Plots by MatLab

Here is an example of doing Bode Plots with Matlab.

Assume you have a small signal circuit like this.

2.1. Find Vout/Vin

Assume you have the following parameters and try to draw the bode plots. First, you need to find out Vout/Vin.

2.2. Plot the Bode Plot with MatLab

Assume that you wanted to use Matlab in order to obtain Bode magnitude and phase plots for the following transfer function. The s is jw (j omega).

H(s) = Z(s)/P(s), where
 Z(s) = [2.5329e-14*s^2 + 1.5915e-4*s + 1]
 P(s) = [2.5329e-20*s^2 + 1.5915e-7*s + 1]

You would need to type the following:
>> num = [2.5329e-14 1.5915e-4 1];
>> den = [2.5329e-20 1.5915e-7 1];
>> sys = tf(num,den)
>> bode(sys,{1,1e15})

Page 4

Page 5

3. Bode Plot by Hand Example

3.1 The Transfer Function

Say we want to plot the following transfer function by hand.

First, we rearrange the numbers

Notice when omega w equals to 4.938 x 1011 , it becomes a corner in the bode plot. Also, if w is close to zero, is just 7.185.

3.1 Magnitude Plot

Just adding all the plots. 20 log(7.185) = 17.126.

+

Page 6

3.2 Phase Plot

Just adding all the plots.

+

4. Reference

Original EE 105 Discussion Notes from Meghdad Hajimorad (“Amin”)

Last Modified by: Bill Hung
Date: 5 August 2006

Page 7

# Text boxes

+

-

+

-

Vin

Rs

Rg

Cgs

+

Vgs

-

gmVgs

Rout

rd

Vout

+

-

>> num = 5.82e6;        %%the numerator

den = [4e-5 8.1e5];       %%the denominator

sys = tf(num, den)       %%the transfer function

bode(sys,{1,1e15})        %%plot the magnitude and phase of the transfer function

%% The frequency range is 1 rad/s to 1e15 rad/s

Transfer function:        %Output

5.82e006

--------------------------

4e-005 s + 810000

17.126

4.938x1011

For 7.185

For

For

For 7.185

4.938x1011